Date:		5/5/2015		Requested By:	Sarah Ballmer

Room No. 	N-612

Telephone No.	225-379-1718

S.P. No. 	H.000263				           Metric    English

450-91

Scale: 1:50

Name:	CHEF MENTEUR BRIDGE AND APPROACHES

Route:	US-90

Parish:	ORLEANS

Limits of Survey

Begin:	4010’ WEST OF THE EXISTING BRIDGE (SEE LAYOUT MAP)

End:	2615’ EAST OF THE EXISTINGE BRIDGE (SEE LAYOUT MAP)

Length:	7675’ TOTAL LENGTH ALONG US-90 (SEE LAYOUT MAP).

Required Width of D.T.M.	170’ AVG. ON US 90, 240’ AT SAN MARCO RD, AND FORT MACOMB RD. AND 400’ AROUND CURVE DATA 4 AND PROPOSED BRIDGE (SEE LAYOUT FOR MORE INFORMATION).

Type of Typical Section:	SUBURBAN ARTERIAL (S-2), TWO 12’ LANES, 8’ SHOULDER, AND 6:1 SIDE SLOPES WITHIN CLEARZONE

Side and Cross Roads:

Length to survey:    Down side roads: 200’

Width of D.T.M.:    80’

down cross roads:		       	Width of D.T.M.:

major intersections:        	Width of D.T.M.:

Will Additional Right of Way Be Required?

If so:	On entire project:		 (SEE LAYOUT MAP)

Specific locations?

Side and/or cross roads?	     SIDE ROAD

Do you want bridge sub-structures located?	YES, (ADDITIONAL REQUEST FOR SUPERSTURCTURE “ENVELOPE”, SUBSTRUCTURE, HYDROGRAPHIC, AND ACOUSTIC SURVEYS.

Is a drainage map required?	 (See Drainage Survey Request Layout for limits)

Will this project be designed:  In House: 	Consultant:

Is survey on:   Existing Alignment,  New Alignment,  Both