Construction Plan Taking Lines

The following is a guide for Road Designers to help expedite and improve the preparation of the Right of Way Maps.

- Although Hilly terrain may cause the limits of construction to vary in and out, set required right of Way lines equi- distant and consistent with the centerline of the project so far as possible – Consideration must be given to utility relocation.

- If the centerline of the project is curved and the required Right of Way lines are equal distances right and/or left of the centerline, keep the required Right of Way lines concentric to the project centerline. Do not make non-tangent or non-concentric curves in the Required Right of Way lines. This includes side-street taking lines.

- When the design requires tying to the required right of way line to existing Right of Way, do not compute the station and offset. Give enough data for the map maker to establish the existing Right of Way and compute this tie. (Show “Tie to Existing R/W” on construction plans.)

- Be sure to show every required Right of Way break tie to the centerline of the project.

- Establish the Existing Right of Way or request that existing Right of way be established during the topographic survey phase of the project if you intend to keep the construction limits within the existing right of way. Apparent Right of Way lines labeled as Required Right of Way lines cause additional title work to be acquired, which causes delays and adds additional expenses to the project which may not be needed.

- When revisions to the required right of way lines are necessary be sure to indicate what revisions have been made in the transmittal letter and by highlighting the changes on the plan and profile sheets. Don’t just send a complete new set of construction plans which must be searched for the revisions.

- When you receive the final mylars of the Right of Way maps to place them into the construction plans, review the Right of Way maps to insure the Right of Way breaks match the construction plans. The Right of Way map MUST match the construction plans. If changes are necessary contact Location and Survey, “A” sheets may be required.

- Do not to allow the Joint Plan Review meeting to be scheduled before the Plan-In-Hand has been held.

- If changes in the required Right of Way Lines are foreseen during the process of setting the “Final Taking Lines” contact the project coordinator and Location and Survey to Stop the contract time for the Right of Way maps